Building Envelope Requirements for Climate Zone 5

| Opaque Elements | Nonresidential |
| --- | --- |
|  | Assembly Maximum | Insulation Min. R-value |
| Roofs |
| Insulation Entirely above Deck | U-0.048 | R-20.0 c.i. |
| Metal Building | U-0.065 | R-19.0 |
| Attic and Other | U-0.027 | R-38.0 |
| Walls, Above-Grade |
| Mass | U-0.090 | R-11.4 c.i. |
| Metal Building | U-0.113 | R-13.0 |
| Steel-Framed | U-0.064 | R-13.0 + R-7.5 c.i. |
| Wood-Framed and Other | U-0.064 | R-13.0 + R-3.8 c.i. |
| Floors |
| Mass | U-0.074 | R-10.4 c.i. |
| Steel Joist | U-0.038 | R-30.0 |
| Wood-Framed and Other | U-0.033 | R-30.0 |
| Slab-On-Grade Floors |
| Unheated |  | No requirement |
| Opaque Doors |
| Swinging | U-0.700 |  |
| Nonswinging | U-0.500 |  |

| Fenestrations | Nonresidential |
| --- | --- |
|  | Assembly Max. U | Assembly Max. SHGC |
| Vertical Glazing |
| Nonmetal framing (all) | U-0.35 | SHGC-0.40 all |
| Metal framing (curtain wall/storefront) | U-0.45 |  |
| Metal framing (entrance door) | U-0.80 |  |
| Metal framing (all other) | U-0.55 |  |
| Skylight with Curb, Glass, % of Roof |
| 0% - 2.0% | U-1.17 | SHGC-0.49 |
| 2.1% - 5.0% | U-1.17 | SHGC-0.39 |
| Skylight with Curb, Plastic, % of Roof |
| 0% - 2.0% | U-1.10 | SHGC-0.77 |
| 2.1% - 5.0% | U-1.10 | SHGC-0.62 |